## Slide 1: ANATOMY OF A HOT AIR BALLOON
Aerospace – Fall 2012

## Slide 2: Anatomy of a Hot Air Balloon
The hot air balloon consists of three parts:
    Envelope
    Basket
    Burner System
There are many differences among balloons made by various manufacturers, so for discussion purposes, we’ll focus on the Raven S-55A, one of the most popular types and sizes of balloon in current use.

## Slide 3: Anatomy of a Hot Air Balloon

## Slide 4: Anatomy of a Hot Air Balloon
Balloons are categorized by the Federation Aeronautique Internationale (FAI), according to how much air their envelopes contain.

## Slide 5: Anatomy of a Hot Air Balloon
THE ENVELOPE
  The part of the aircraft that looks like a balloon is actually called an envelope.
  Some pilots affectionately refer to it as “the bag”. (balloon, envelope and bag are all terms for the same thing)
  It is connected to the gondola, or basket (in which the pilot and passengers ride) by stainless steel suspension cables.

## Slide 6: Anatomy of a Hot Air Balloon
THE ENVELOPE FABRIC
  The fabric in the envelope is rip stop, fire-resistant nylon, similar to material used in the backpacks or lightweight tents carried by hikers and mountaineers.

## Slide 7: Anatomy of a Hot Air Balloon
THE ENVELOPE GORES
  It is woven in panels, two panels making up what is a gore.
  There are 24 of these gores, or large vertical sections, in the entire S-55A envelope.
  The gores are held together by stitching and by heavy duty load tapes (like seatbelt material) which help support the weight of the balloon and minimize strain on the fabric.

## Slide 8: Anatomy of a Hot Air Balloon
THE ENVELOPE
The envelope is usually treated with a polyurethane coating to reduce porosity (air leaking out).
The coating also contains an ultraviolet inhibitor (sun screen) to help the fabric withstand the rays of the sun.

## Slide 9: Anatomy of a Hot Air Balloon
THE TOP CAP OR CROWN
The top cap or crown of the balloon may be designed in one of two ways.
  The STANDARD TOP
  The PARACHUTE TOP

## Slide 10: Anatomy of a Hot Air Balloon
THE STANDARD TOP
  Circular deflation port that is closed off by a circular panel.
  The port is sealed during flight by a flexible hook and loop closure (velcro)
  The deflation port line – called the rip line – is red, and extends from the top to the basket and pulled by the pilot upon landing for instant deflation of the envelop.
  Pull on the line, the velcro opens, the hot air rushes out.

## Slide 11: Anatomy of a Hot Air Balloon
THE PARACHUTE TOP
  Also has an opening in the crown, along with a similar circular panel to fill the opening. BUT…
  The panel is rigged up with lines, as the name suggests, exactly like a parachute.
  It is used to completely deflate the envelop after landing, AND…
  It is used during flight to vent a limited amount of hot air as a means for controlling vertical ascent or descent.

## Slide 12: Anatomy of a Hot Air Balloon
THE SKIRT
Connected to the bottom section of the envelope with peelable tabs and helps create a stovepipe effect when the burner system is running, channeling the warm air into the balloon and improving fuel efficiency – especially on windy days, by protecting the burner from the wind.

## Slide 13: Anatomy of a Hot Air Balloon
THE TELLTALES
Temperature indicators that are attached to the inside of the balloon envelope, near the top or crown.
The telltales are white when installed, but turn black if the air in the envelope gets too hot.
The pilot uses these to tell at a glance when the balloon may need repair.

## Slide 14: Anatomy of a Hot Air Balloon
THE BASKET
Currently, open-air passenger vessels for balloons (the baskets) are made of either wicker or aluminum and fiberglass.
A rigid tubular framework extends from the basket upward where it attaches to the 24 stainless steel cables suspended from the envelope.

## Slide 15: Anatomy of a Hot Air Balloon
THE BASKET
Wicker is the classic or traditional look in a basket, but it is actually not nostalgia that makes it so popular.
The strong and resilient rattan that is woven around a tubular aluminum frame is an excellent shock absorber during not-so-perfect landings.
The aluminum/fiberglass baskets are quite strong and lighter than wicker, but don’t absorb energy.

## Slide 16: Anatomy of a Hot Air Balloon
THE BASKET
This rigid framework actually serves three purposes:
  It helps protect passengers
  It supports the burner system, which is installed overhead at the top of the basket
  Thanks to the mechanical-fulcrum effect, it provides the basket with stability and less of a tendency to tip over upon landing.

## Slide 17: Anatomy of a Hot Air Balloon

## Slide 18: Anatomy of a Hot Air Balloon
THE BASKET
Baskets normally come in square or rectangular shapes – triangular shapes are also available.
  You can even special order completely enclosed gondolas with built in seats and champagne holders!
The basket MUST have room for securing the necessary fuel tanks and flight instruments.

## Slide 19: Anatomy of a Hot Air Balloon
THE BURNER SYSTEM
The third major component, the burner system, is the motive force for the balloon.
It produces the heated air which the pilot uses to lift off and to control the vessel’s up-and-down motion once aloft.
The burner system normally points directly into the center of the balloon envelop.

## Slide 20: Anatomy of a Hot Air Balloon
THE BURNER SYSTEM
There is a blast valve allowing the pilot to adjust the rate at which fuel flows from the tanks.
To draw fuel into the burner, the pilot simply pulls the trigger on his blast valve. The liquid propane gas is carried under pressure from the fuel tank to the burner, where it is set on fire by the pilot light.
A pressure gauge on the burner tells what the pressure is.

## Slide 21: Anatomy of a Hot Air Balloon
THE BURNER SYSTEM
When the pilot light ignites the vapor, it sends a six-to eight-foot flame into the envelope, making a loud whooshing sound and adding heat at the rate of 12 million BTU's (British Thermal Units) per hour.
The BTU is defined as the quantity of heat required to raise the temperature of one pound of water by one degree Fahrenheit.

## Slide 22: Anatomy of a Hot Air Balloon
THE BURNER SYSTEM
To give a better idea of the tremendous output of a burner system in a hot air balloon, one burner produces at a rate per hour that would be enough to heat 120 three bedroom homes comfortably.

## Slide 23: Anatomy of a Hot Air Balloon
THE BURNER SYSTEM
There are two ways of heating air inside the envelope.
  One is by triggering the blast valve, as mentioned, which when wide open can add heat at the rate of 12 million BTU's per hour.
  Intermittent blasts during flight enable the pilot to maintain a standard temperature in the balloon, and a standard temperature generally provides a standard altitude for that flight.

## Slide 24: Anatomy of a Hot Air Balloon
THE BURNER SYSTEM
The second method of adding heat to the envelope is by using the "cruise" or metering valve.
  By monitoring the exact flow of propane to the burner, you can then maintain a steady output from the burner, which will provide a standard temperature.
  This would enable you to maintain a straight and level flight without having to touch the blast valve that often. It's as close as you can come to flying on automatic pilot in a hot air balloon.

## Slide 25: Anatomy of a Hot Air Balloon
Other Ballooning Gear -- Required Equipment
Altimeter: This tells you how high you are above the ground, normally giving readings in feet above sea level, and can be adjusted to the local ground elevation where the ascent is taking place.
Variometer: This is basically a rate of-climb meter and lets you know first of all if you are moving up or down.
  That may sound ridiculous, but at altitudes of 1,000 feet or more, where visual references are few and far between, it is often quite difficult to judge such basic facts of life as whether you are on the way up, or on the way down.
  The variometer also measures the vertical speed of the balloon in feet per minute or second.

## Slide 26: Anatomy of a Hot Air Balloon
Other Ballooning Gear -- Required Equipment
Pyrometer: An electrical sensor installed near the top or crown of the envelope sends information to this meter in the basket. It tells the temperature of the air in that area.
  As with RPM's in an automobile, there is a "red line" not to exceed in terms of envelope temperature, beyond which you risk damaging fabric strength. The pyrometer helps you monitor this important factor.
Fuel gauge: This shows how much propane is left in the tanks on board, and because fuel supply is important to a safe and sane balloon flight, such gauges should be as reliable and visible as possible.

## Slide 27: Anatomy of a Hot Air Balloon
Other Ballooning Gear -- Required Equipment
Sparker: This gadget comes in handy for quickly reigniting a pilot light that has inadvertently gone out.
  Most pilots carry two sparkers-plus a cigarette lighter and a pack of dry matches, to be on the safe side Sparkers are also used by welders and by campers for starting up Coleman lanterns, so they are readily available.
Headgear: Protective hats or helmets are vital safeguards in the event of a fast or bouncy landing. As with lifeboats on a ship, there should be enough on board for all occupants.

## Slide 28: Anatomy of a Hot Air Balloon
Recommended Equipment
Protective Clothing: There is no point in totally ignoring the remote but real chances for injury involved in ballooning. In that spirit, let's note a few simple precautions to incorporate in your standard garb for the sport.
    The pilot should wear some eye protecting device-goggles or simply a pair of sunglasses-during the inflation stage. This will shield his eyes from any backlash of heat from an unexpected gust of wind blowing flames from the burner toward him instead of toward the envelope, and conceivably save a nice set of eyebrows.

## Slide 29: Anatomy of a Hot Air Balloon
Recommended Equipment
  Pilot and crew should wear heavy-duty gloves as protection from the heat of the burner and its flames, and also from possible rope burns.
  Pilot and crew should wear long sleeved shirts and long pants, again to protect themselves from the heat and flame of the burner system during inflation, cotton or fire-retardant materials are preferred, not nylon and polyester.
  Pilot, crew, and passengers should wear sturdy boots or high shoes so everyone is more comfortable in the rough or slippery terrain one might conceivably land in.

## Slide 30: Anatomy of a Hot Air Balloon
Recommended Equipment
Fire Extinguisher: It should be of the type useful in combating propane fueled fires, and carried not only in the chase vehicle but on board balloon. The 2A10BC is the type often recommended.
First Aid Kit: It should include silver compound medication for burns and, like the fire extinguisher, be carried both on board and in the chase vehicle.
Balloon Log Book: The pilot records the date, place, and other pertinent details of every one of his flights in the given balloon.

## Slide 31: Anatomy of a Hot Air Balloon
Optional Equipment
Electric Blast Valve: This is a push-button valve control that can be operated from anywhere in the basket.
Electronic Ignition: Similar to above, this operates off a battery and keeps the pilot light going.
Compass: Until recently, FAA regulations required balloonists to carry a magnetic compass on board, but this device plays no practical role, at least not on short flights. On long flights in unfamiliar country, it does give you an idea of the exact direction in which you are gradually getting lost.
Communication System: On short flights there is no particular need to be in touch with Houston Control. Aviation radios and transponders are useful on board for long flights at high altitudes, and radios are required to be carried if you are flying through any airport traffic control zone.